## Slide 1
Stall-Triggered Policy Switching for
DRL Navigation in Trap Scenarios
Composing complementary policies at runtime to eliminate catastrophic navigation failures
[Author Name] · [University Name] · Summer Research 2026
94%
Scenario avg SR
(+27 vs baseline)
88%
Standard env SR
(matches baseline)
0
Catastrophic
failures (0% cells)
0
Additional
training cost
1
Problem: DRL fails in traps
DRL navigation achieves high success in open environments but completely fails (0% SR) in trap scenarios requiring temporary retreat from the goal.
2
Key finding: exploration-precision conflict
Exploration bonus fixes U-trap (0→83%) but destroys narrow door (100→0%). Annealing recovers narrow door but loses U-trap. Irreconcilable.
Method
Std
U-trap
Narrow
Avg
Baseline
87%
0%
100%
67%
Curriculum only
74%
0%
8%
52%
Exploration (πE)
80%
83%
0%
71%
Annealed (πP)
82%
0%
100%
75%
No single policy avoids all 0% cells
3
Method: Stall-Triggered Policy Switching (STPS)
Main mode
Execute precision policy πP
(standard navigation)
DEFAULT
Escape mode
Execute exploration policy πE
(novelty-seeking navigation)
TEMPORARY
Stall: ‖xₜ − xₜ₋₂₀‖ < 0.15m
OR oscillation ≥ 5 reversals/12 steps
Escaped: k ≥ 120 AND ‖xₜ − xsw‖ > 0.5m
1
Zero training cost
Both policies frozen; only runtime logic
2
Negligible overhead
One distance check per step (<0.1ms)
3
Real-robot ready
Simple if-else, no GPU for switching
4
Results: STPS outperforms all single policies
Method
Standard
(100 ep)
S1
U-trap
S2
Double-U
S3
Narrow door
S5
Corridor
Scenario
avg
CNNTD3 baseline
87%
0 ± 0%
69 ± 4%
100 ± 0%
100 ± 0%
67%
RCPG (GRU)
88%
0 ± 0%
0 ± 0%
75 ± 0%
100 ± 0%
44%
Curriculum only
74%
0 ± 0%
100 ± 0%
8 ± 0%
100 ± 0%
52%
Exploration (πE)
80%
83 ± 0%
100 ± 0%
0 ± 0%
100 ± 0%
71%
Annealed (πP)
82%
0 ± 0%
100 ± 0%
100 ± 0%
100 ± 0%
75%
STPS v2 (ours)
88%
75 ± 7%
100 ± 0%
100 ± 0%
100 ± 0%
94%
3 seeds × 12 perturbed starts. STPS is the only method without any 0% catastrophic failure.
5
Success and failure case analysis
Failure: Baseline
in U-trap
SR = 0%
Failure: πE
in narrow door
SR = 0%
Failure: Annealed
U-trap reverts
SR = 0%
Success: STPS
U-trap escape
SR = 75%
Success: STPS
narrow door
SR = 100%
Success: STPS
std env
SR = 88%
6
Parameter sensitivity
U-trap SR (%) / Narrow-door SR (%)
K=120, δ_prog=0.5m fixed
δ=0.10
δ=0.15
δ=0.20
W=15
42/100
42/100
67/100
W=20
67/100
67/100
67/100
W=30
0/100
17/100
25/100
Narrow door = 100% across entire grid
→ switching never harms precision
7
Error taxonomy and what didn't work
Greedy tracking
Cannot retreat — Baseline in U-trap
Reward conflict
Exploration vs precision — πE in narrow door
Parameter space limit
Single network can't encode both — Annealing
Detection latency
20 steps to confirm stall — STPS 75%<83%
What didn't work:
• STPS v3 (goal-distance + progressive escape): no gain over v2
• U-trap specialist: 83%, same as original improved
• Bottleneck = geometric difficulty, not detection/model
8 Conclusion
We revealed a hard exploration-precision conflict in DRL navigation and proposed STPS, a training-free switching architecture.
STPS achieves 94% scenario average — the only method without catastrophic failure — while matching baseline on standard environments (88%).
9 Future work
1. Real-robot deployment on LIMO platform
2. Learned switch trigger (RL scene classifier)
3. Extend policy library beyond two modes
4. Isaac Lab parallel training
5. PINN-based delay compensation
Code and data available | Contact: [email] | Summer Research Program 2026